## Slide 1
Design of Real Time weather monitoring instrument using Internet of thing Module
Prof. Dr. Chandan Sarangi
Dept. of Civil Engineering
IIT Madras
Sougat kr. Sarangi (CE21D300)
Abhishek kishor (CE23E009)
Shakeel Ah. lone (CE23E012)

## Slide 2
Objective Design & Development of Wind anemometer, Rain gauge and vane Integration of sensor with IOT Board Internet of thing Real time Weather monitoring | Workflow
Learning How meteorological instruments work Analysis and Design Internet of things Computer aided design | 
Objective
Stop
Level 5
Level 4
Level 3
Level 2
Design Constraint
Computer Aided Design & Simulation
Sensor integration & Testing
Individual Hardware interfacing & Testing
Level 1
Start
Embedding:Iot into sensor network
Literature survey & Market study
Sensor Calibration & Data validation

## Slide 3
Arduino Board
NETWORK
ES8266
Wind Direction
North East / 45°
Wind speed
2.4 m/s
Rainfall
15 mm
POWER SOURCE (DC SOURCE)
APPLICATION
Block Diagram
PROCESSING
Design of Real Time weather monitoring instrument using IOT module

## Slide 4
cup Anenometer
 | Design constraint Cup Anemometer factor (K) | 
four-cup anemometer developed by Robinson of Ireland in 1846. Pindado (2012) Test 21 different cup & arm model and find analytical model of Kondo et al.(1972) was proved to be accurate So, Observations from Lindley(1975) and pindaDo (2012)suggest that K factor to be 0.4. |  | 
Cup Anemometer
Cup arm
Source : D. Lindley(1975)
Proximity Sensor
3 - cup anemometer

## Slide 5
cup Anenometer
Rain Guage
Funnel
Ultrasonic sensor
Graduated
cylinder
Dc Pump

## Slide 6
Gray Coded Optical Encoder
Shaft
Vane
LED
LDR
Shaft
Code Disc
Future work

## Slide 7
References
Avallone, E. et al. (2019) ‘An inexpensive anemometer using Arduino board’, Facta universitatis - series: Electronics and Energetics, 32(3), pp. 359–368. doi:10.2298/fuee1903359a.
Carlos-Mancilla, M.A. et al. (2020) ‘Educational mechatronics and internet of things: A case study on dynamic systems using meiot weather station’, Sensors, 21(1), p. 181. doi:10.3390/s21010181.
Coquilla, R.V., Obermeier, J. and White, B.R. (2007) ‘Calibration procedures and uncertainty in wind power anemometers’, Wind Engineering, 31(5), pp. 303–316. doi:10.1260/030952407783418720.
Lindley, D. (1975) ‘The design and performance of a 6-Cup anemometer’, Journal of Applied Meteorology, 14(6), pp. 1135–1145. doi:10.1175/1520-0450(1975)014&lt;1135:tdapoa&gt;2.0.co;2.
Pindado, S., Cubas, J. and Sorribes-Palmer, F. (2014) ‘The cup anemometer, a fundamental meteorological instrument for the wind energy industry. research at the IDR/UPM Institute’, Sensors, 14(11), pp. 21418–21452. doi:10.3390/s141121418.
Sharifabad, H.K., Mirzaei, O. and Talebi, M.H. (2011) ‘Design anemometer with transistor’, Applied Mechanics and Materials, 110–116, pp. 2628–2630. doi:10.4028/www.scientific.net/amm.110-116.2628.
Sheppard, P.A. (1940) ‘An improved design of cup anemometer’, Journal of Scientific Instruments, 17(9), pp. 218–221. doi:10.1088/0950-7671/17/9/301.
Anemometer

## Slide 8
RESULTS DEMONSTRATION

## Slide 9
Thank You

## Slide 10
Questions?

## Slide 11
Final model
Rain gauge
Vane
Anemometer
Proposed CAD Model